## Slide 1
Cable-driven Soft Finger Simulation
Nguyen Dang Doanh 202418423

## Slide 2
  PROJECT OVERVIEW
  PHYSICAL MODEL & FOUNDATION
  DESIGN & IMPLEMENTATION
  RESULTS & EVALUATION
  CONCLUSION
Table of contents

## Slide 3
Project Overview
Simulation Objective: Simulate a soft finger controlled by cable actuation. Observation: Observe the deformation of the elastic material under pulling forces.
Analysis: Analyze the effect of material stiffness on the bending amplitude of the finger.
Simulation Platform: SOFA (Simulation Open Framework Architecture) combined with the SoftRobots plugin.
Core Method: Finite Element Method (FEM) for highly accurate physical simulations.
Versions Used: Python 3.12.1 and SOFA v26.06.

## Slide 4
Source code structure
  Mesh directory: Stores 3D geometric file formats for finite element calculation (.vtk) and graphic visualization (.stl).
  FingerwithSTLIB.py: Main file for Scene Setup and integrated Controller.
  Setup Function: Contains the createScene(rootNode) function to build the SOFA Scene Graph.

## Slide 5
Physical model and foundation
Dynamics Model: Initializes the soft-finger dynamics using FEM with elastic material.
Boundary Conditions: BoxROI fixed boundary.
Total Mass: 0.05 kg.
Poisson’s Ratio: 0.45 (silicone/rubbery material).
Young’s Modulus: 400 kPa (default stiffness).
Gravity: 0.0, -9810.0, 0.0 mm/s² along the -Y-axis.

## Slide 6
Design and implementation
  Cable Actuator: Sets up the pulling cable actuator using CableConstraint
  Coordinate Mapping: Uses BarycentricMapping
  Controller Integration: Integrates a custom class inheriting from Sofa.Core.Controller
  Event Listening: Listens to simulation time step events (onAnimateBeginEvent)
  Calculation: Automatically calculates and updates the cable contraction value using a smooth Cosine wave function
  Maximum Displacement: The actuator has a maximum cable pull displacement of 40.0 mm

## Slide 7
Simulation flowchart

## Slide 8
Results and evaluation
Study Objective: Investigating the effect of Material Stiffness (youngModulus) while keeping the maximum cable pull stroke constant at 40 mm

## Slide 9
Conclusions and limitations
  No Physical Interaction (Collision): The current model does not prevent self-collision if the finger is bent excessively.
  Cable Simplification: The cable is simulated ideally, ignoring friction between the cable and the internal cavities of the finger wall.
  Design Constraints: The finger is a solid block, lacking the bellows structure commonly seen in reality to optimize the bending angle.
  Ideal Actuation Assumptions: The simulation assumes an idealized cable pull with instantaneous response and infinite force. It does not account for the electromechanical constraints of a real actuator system, such as motor torque limits, inertia, or signal delays within the physical control loop.

## Slide 10
Future developments
  Physical Prototyping: Transition from simulation to physical manufacturing using 3D printed molds to cast silicone, allowing for a direct comparison between the FEM simulation and real-world kinematic behavior.
  Controller Upgrade: Implement a closed-loop control system to replace the current open-loop cosine function, enabling more precise trajectory tracking.

## Slide 11
Thank You